Thanks for ordering from Treadmilldoctor.com!

Please review the following important information regarding your purchase of a walking belt for your treadmill.

The installation instructions are rolled up in the walking belt. To retrieve the instructions, remove the rubber band and unroll the belt.

Do not install a new walking belt on a worn deck. Deep grooves or exposed wood can quickly ruin a new belt. Damage to a walking belt from a worn deck is not covered under our warranty.

Before installation of walking belt, ensure both the deck and the rollers are thoroughly cleaned. We typically recommend mineral spirits to clean the deck and rollers. Dirt or other foreign substances transferred to the new walking belt voids the return privilege and cancels any warranty on the walking belt.

Make sure not to over tighten the walking belt or motor belt. Over tightened belts raise the operating amp level which can damage the motor and/or controller. The walking belt should be able to be lifted 3” in the center of the belt along the edge. The motor belt should be able to be twisted by hand almost 90° from its normal operating position.

The additional application of TreadmillDoctor World Famous Lube is for use approximately six months after installation of the new walking belt. The enclosed walking belt is pre-lubed and does not require any additional lubrication at this time.

For questions or concerns regarding the installation of the walking belt please contact our support and service team at doc@treadmilldoctor.com.

We appreciate your business!

Thanks for ordering from Treadmilldoctor.com!

Please review the following important information regarding your purchase of a motor controller for your treadmill.

Most controller failures are a result of a power surge or worn walking belt. Damage to a new controller due to a worn walking belt or a power surge voids any warranty or return.

A new controller should be installed in conjunction with a surge suppressor. If this is not an option, the treadmill should remain unplugged between uses. If your treadmill is made by ICON, we suggest disconnecting power when not in use.

The following six steps make replacing the controller very easy.

- Remove the covering over the controller.

- Remove the screws that mount the controller (LEAVE ALL WIRES IN PLACE).

- Mount the new controller to the treadmill.

- Swap wires one by one from old controller to new controller.

- Calibrate (if necessary).

- Replace the plastic covering.

Many controllers require calibration before they will work or work properly. Refer to the tech sheet, our troubleshooting section online, or email us at doc@treadmilldoctor.com for calibration instructions.

For any questions or concerns regarding the installation of the controller please contact our support and service team at doc@treadmilldoctor.com.

We appreciate your business!