Walking Belt Instructions

Please review the following important information regarding your purchase of a walking belt for your treadmill.

The installation instructions are rolled up in the walking belt. To retrieve the instructions, remove the rubber band and unroll the belt.

Do not install a new walking belt on a worn deck. Deep grooves or exposed wood can quickly ruin a new belt. Damage to a walking belt from a worn deck is not covered under our warranty.

Before installation of walking belt, ensure both the deck and the rollers are thoroughly cleaned. We typically recommend mineral spirits to clean the deck and rollers. Dirt or other foreign substances transferred to the new walking belt voids the return privilege and cancels any warranty on the walking belt.

Make sure not to over tighten the walking belt or motor belt. Over tightened belts raise the operating amp level which can damage the motor and/or controller. The walking belt should be able to be lifted 3” in the center of the belt along the edge. The motor belt should be able to be twisted by hand almost 90° from its normal operating position.

The additional application of TreadmillDoctor World Famous Lube is for use approximately six months after installation of the new walking belt. The enclosed walking belt is pre-lubed and does not require any additional lubrication at this time.

For questions or concerns regarding the installation of the walking belt please contact our support and service team at doc@treadmilldoctor.com.

Thank you for choosing Treadmill Doctor!